## Slide 1
Standard Update/Changes Cornell Design and Construction Standards 260923 Lighting Controls Design Standard
Erich Reichard(ETR33)
Facilities Engineering
November 2022

## Slide 2: History
Previous version – dating back to 2016
  FE collaboration with former Director of Utilities and Distribution and Energy Management Lanny Joyce
  Goal was to remove proprietary systems, specifically Lutron Quantum
Gates Hall
  Lutron Quantum wanted to charge for software upgrade, server hardware, single workstation for control
  Legacy systems installed in Gates as well as other buildings
  Cornell refused to pay for the upgraded software
  Created conversation for all controls on Building Automated Control System (BACS)
Lighting control on BACS gave Cornell control of any changes

## Slide 3: Types of Systems – Previous Terminology
Integrated
  Connected and controlled through BACS
Stand alone
  Controlled by individual components using low voltage or wireless
  No connection to any other rooms or spaces. No internet, building control connections
Networked
  Stand alone systems connected through hubs/nodes to network devices together using ethernet, wireless or proprietary networks

## Slide 4: BACS Controlled Lighting System
Wall Switch
Light Fixture
Relay
Control Wiring
Control Wiring
Power Wiring
Power Wiring
To Building Automation Control System
Control Module
Control Wiring
Control Wiring
Occupancy/Vacancy Sensor

## Slide 5: Stand Alone System
Wall Switch
Occupancy/Vacancy Sensor
Light Fixture
Power Pack/Relay
Power Wiring
Control Wiring
Control Wiring
Control Wiring
Power Wiring

## Slide 6
Who were the primary authors/editors of the revised standard?
FE Electrical Engineer Chris Wayman and myself were primary authors in collaboration with:
  FE Mechanical – Senior Mechanical Engineer Elizabeth Kolacki and Mechanical Section Leader Jim Feeley
  Utilities/E&S – Former Director of Utilities and Distribution and Energy Management Mark Howe and current interim Director of Utilities and Distribution and Energy Management Cole Tucker
  FCS Control Shop – Controls Shop Manager Dustin Darnell and Controls Shop DDC Applications Designer Jason Arnold
260923 Lighting Controls Design Standard

## Slide 7
Why did we update the standard?
FE reviews all standards every two years
Cost implications
Maintenance implications
Applying lessons learned NCRE and other recent projects
Confusion over previous standard
University Stewardship
260923 Lighting Controls Design Standard

## Slide 8
Reduce up-front cost
Less wiring for control points
No programming for input/output
Recently BACS control was valued out of most spaces in CIS, which greatly lowered upfront cost for lighting control
Less Maintenance
Less troubleshooting and programming for changes in future by Controls Shop
Devices replaced by Zone Electricians, will not require reprogramming
Cost Implications, Installation Impacts

## Slide 9
Major Changes:
Simplified control in most spaces – Offices, classrooms, laboratories, etc.
260923 Lighting Controls Design Standard
BACS controlled lighting only in specific spaces – animal rooms, plant growth rooms, atriums and corridors

## Slide 10: Thank you! Questions?
Please contact me with questions or comments:
Erich Reichard
etr33@cornell.edu
607-255-3934