## Slide 1: Cornell Sprinkler Retrofit Initiative
Tom Jordan FPE, PMSFPE
Facilities Engineering
March 23, 2023

## Slide 2
February 23rd, 1991
ONE MERIDIAN PLAZA, PHILIDELPHIA
  Built in 1973
  38-stories
  Non-sprinklered
  Fire began on 22nd floor around 8:20PM
  Source - construction-related linseed oil rags
  Multiple factors lead to an out-of-control fire:
    Delayed reporting to Fire Department
    Water supply issues
    Improperly inspected, tested and maintained standpipe system
    Improperly separated shafts/floors allowed smoke and fire to pass from floor to floor
  Three fire fighters perished
  Fire fighting continued for 11 hours - had to be abandoned at 7AM, the next day, due to structural failure concerns
  Retrofitted sprinklers on 30th floor stopped the fire the next day at around 3PM
  Prompted creation of sprinkler retrofit laws
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 3
Fire Protection Systems Overview
On the Ithaca campus there are:
  Over 200 sprinkler systems (Archives, Athletics, Classrooms, Dorms, Offices, Labs, Storage)
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 4
Fire Protection Systems Overview
On the Ithaca campus there are:
  A mix of wet- & dry-chemical, gaseous, & foam systems (Fuel Dispensing and Storage, Kitchens, Ornithology, Server Rooms)
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 5
A Brief Code History
In early to mid 20th century sprinklers were provided consistently in older buildings with combustible construction.
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 6
A Brief Code History
With the advent of non-combustible “fire-safe” construction - Codes required sprinklers only in specific areas (storage, exits).
The majority of buildings from that era were either non-sprinklered or partially sprinklered.
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 7
A Brief Code History
1980s - Code requirements were focused more on compartmentalization and fire separation.
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 8
A Brief Code History
Early 2000s – Significant changes to building construction codes placed more importance on sprinkler protection and provided incentives to the owner (code advantages) when sprinkler protection is provided throughout.
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 9
A Brief Code History
Most buildings on campus are classified by Building Code as Business Occupancy, which are not required to have sprinkler protection.
However:
  Cornell has been proactively providing sprinkler protection in all new construction and in renovated areas when feasible.
  Factory Mutual Global (Cornell’s insurance underwriter) desires sprinklers in all facilities.
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 10
What Makes a Building High-Risk?
Construction Type
  Combustible structures (wood) are more suspectable to fire spread and premature structural failure
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 11
What Makes a Building High-Risk?
Height
  Taller buildings act like chimneys, which promotes smoke and fire spread to the upper floors
  More difficult for occupants (and fire fighters) to escape and be rescued
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 12
What Makes a Building High-Risk?
Occupancy Type
  Lab buildings contain hazardous flammable/combustible solids, liquids, and gases
  Increases probability of a fire occurring and accelerated fire growth
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 13
What Makes a Building High-Risk?
Smoke & Fire Separations
  Older buildings tend to promote the passage of smoke and fire more-easily to other parts of the building
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 14
What Makes a Building High-Risk?
Sprinkler Protection
  A building without a sprinkler system has a much greater probability of experiencing a total loss
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 15
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities
Purpose of Initiative
Update sprinkler/standpipe database for all Cornell owned & operated buildings.
Identify buildings with greatest fire hazards and greatest impacts to operation, via collaboration with EH&S.
Advocate for the retrofitting of sprinklers in Cornell’s riskiest buildings.
Provide support to the project management teams tasked with implementing sprinkler retrofits

## Slide 16
Sprinkler Status for Ithaca Campus (All Buildings)

## Slide 17
Sprinkler Status for Ithaca Campus (Laboratory Buildings)

## Slide 18
Top Ten Buildings and Current Status
ST Olin – Sprinkler System In design
Vet Research Tower – Consultant selection underway
Baker Lab – Retrofitted on an as-renovated basis
Boyce Thompson – Forthcoming study
Clark Hall – Retrofitted on an as-renovated basis
Morrison Hall – No activity as of yet
Barton Hall (Geneva) – Consultant selection underway
Corson-Mudd – Sprinkler System In design
Phillips Hall – Forthcoming design
Hollister Hall – No activity as of yet
Wilson Lab – Sprinkler System In design
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 19
One Two Last Things…
SUBMITTALS
&
INSPECTIONS
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities

## Slide 20
QUESTIONS?
Cornell Sprinkler Retrofit Initiative
Ithaca & Geneva Campuses, and all other Cornell Owned and Operated Facilities